## Slide 1
Ranger 3.0 Troubleshooter
Start
Power Related Related Error
Ver.1.0
Note:
Run the slide and click on buttons, videos or hyperlinks as necessary. DO NOT USE ARROW KEYS
In case of incorrect selection, rerun the slide or go to previous slide
FlowChart Reference

## Slide 2
Ranger 3.0 Troubleshooter
S N | Error Flag | Bit Name | Error Description | Reference Link for Resolution | Remarks
1. | NA | NA | Enable to Login into Ranger |  | 
2. | NA | NA | Bot is not Powering Up. |  | 
Click
Click

## Slide 3
Ranger 3.0 Troubleshooter
Available Version
Ver 1.0
Power Related Errors

## Slide 4
Ranger 3.0 Troubleshooter
Start
Power Related Error
Ver.1.0
Note:
Run the slide and click on buttons, videos or hyperlinks as necessary. DO NOT USE ARROW KEYS
In case of incorrect selection, rerun the slide or go to previous slide
FlowChart Reference

## Slide 5
Ranger GTP 3.0 Troubleshooter
Previous
Power Related Issue
Ranger Login Issue
Ranger Not Powering Up or Dead Issue
Button
Button
Press the respective Button for troubleshooting the issue.
Note: Press the Ranger Login Issue Button when we are unable to login into the Ranger through IP or Ranger is frequently disconnected.
Note: Press the Ranger Not Powering Up or Dead Issue Button when Ranger is not powering up after pressing the ON/OFF switch of Ranger or Ranger is showing Dead in D3 map.
Note: If we do not have Ranger Login and Ranger not Powering up related issue, we should not use this document.

## Slide 6
Ranger 3.0 Troubleshooter
Ensure that your laptop should be connected with “gorwifi” network. Reference Image is below mentioned.
Preview
Next
Is your laptop is connected with “gorwifi” network?
YES
NO

## Slide 7
Ranger 3.0 Troubleshooter
If your network is not connected with “gorwifi” network, connect your laptop with “gorwifi” network.
Again restart the Ranger and check if the issue is resolved.
Preview
Next
Is your login issue fix?
YES
NO

## Slide 8
Ranger 3.0 Troubleshooter
Check Moxa led status as mentioned in support link document.
Restart the Ranger and check if the issue is resolved
YES
NO
Is your issue fix?
SN | Support Link
1 | Procedure to Check Moxa Led Status
Preview
Next

## Slide 9: Procedure to Check Led Status of MOXA
Prepared by Rishabh – ME Team
Copyright © 2019 GreyOrange
SN | Version | Prepared / Revised | Checked / Approved |  | Ref Details
1 | 1.0 | Rishabh | Shrinidhi/Anand |  | 
Purpose of Document : Explain the step by step procedure to check the led status of MOXA at customers sites.

## Slide 10: Procedure to Check Led Status of MOXA
Tools Required :
SN | Item Details | Qty | Photo | Reference Purchase Link
1 | Bit Driver | 1 Nos. |  | https://www.lowes.com/pd/LENOX-6-Piece- Plastic-Handle-Magnetic-Multi-Bit- Screwdriver-Set/1000498761
2 | Bit adaptor | 1 Nos. |  | https://www.amazon.com/uxcell-4-Inch- Drive-Socket- Steel/dp/B07BHFWKDK/ref=sr_1_11?dchild =1&keywords=1%2F4- Inch+Drive+8mm+Hex+Bit+Socket&qid=159 4815613&sr=8-11
3 | Hex Metric M3, bit | 1 Nos. |  | https://www.amazon.com/Wiha-71397- Metric-Insert-6- Piece/dp/B0084B7S70/ref=sr_1_4?dchild=1 &keywords=hex%2Bbits%2Bmetric&qid=15 94814886&sr=8-4&th=1
4 | Gloves | 1 Nos. |  | https://www.uline.com/Product/Detail/S- 15357M/Anti-Static-Gloves/ESD-Gloves- Fingertip-Coated-Medium?model=S- 15357M&RootChecked=yes

## Slide 11: Procedure to Check Led Status of MOXA
Manhour Details:
Prepared by Rishabh – ME Team
Copyright © 2019 GreyOrange
Activity Name | No. of Required operator | Time Taken
Procedure to Check MOXA led status | 01 | 7 mins

## Slide 12: Procedure to Check Led Status of MOXA
Prepared by Rishabh – ME Team
Copyright © 2019 GreyOrange
Safety Precaution:
Turn- OFF the Ranger before starting activity.
Use ESD gloves at all times while performing maintenance work.
Activity should be performed away from Moisture & dust area.
Do not remove any other wires from Ranger while doing the activity.

## Slide 13
Prepared by Rishabh – ME Team
Copyright © 2019 GreyOrange
Step to be followed

## Slide 14: Procedure to Check Led Status of MOXA
Turn OFF the Ranger by pushing ON/OFF button.
Now move the Ranger on the service lift.
Open front side shell assembly.
ON/OFF button
Front Side Shell

## Slide 15: Procedure to Check Led Status of MOXA Turn- ON the Ranger. Now check the moxa led (sys led) status. It should be blinking as green color. If it is blinking red color, it means something is problem either harness connections, IMB board or moxa.
SYS led Green color blinking

## Slide 16
END
Return back to error slide for further troubleshooting
Next

## Slide 17
Ranger 3.0 Troubleshooter
Check Moxa connections as mentioned in support link document.
Click on next tab.
SN | Support Link
1 | Procedure to Check Moxa Connection
Next

## Slide 18: Procedure for Moxa Harness Check
SN | Version | Prepared / Revised | Checked / Approved |  | Ref Details
1 | 1.0 | Rishabh | Asheesh | Shrinidhi | 
Purpose of Document: Explain the step by step procedure to check moxa related harness at customer site.

## Slide 19: Procedure for Moxa Harness Check
Tools Required :
SN | Item Details | Qty | Photo | Reference Purchase Link
1 | Bit Driver | 1 Nos. |  | https://www.lowes.com/pd/LENOX-6-Piece- Plastic-Handle-Magnetic-Multi-Bit- Screwdriver-Set/1000498761
2 | Bit adaptor | 1 Nos. |  | https://www.amazon.com/uxcell-4-Inch- Drive-Socket- Steel/dp/B07BHFWKDK/ref=sr_1_11?dchild =1&keywords=1%2F4- Inch+Drive+8mm+Hex+Bit+Socket&qid=159 4815613&sr=8-11
3 | Hex Metric M3, bit | 1 Nos. |  | https://www.amazon.com/Wiha-71397- Metric-Insert-6- Piece/dp/B0084B7S70/ref=sr_1_4?dchild=1 &keywords=hex%2Bbits%2Bmetric&qid=15 94814886&sr=8-4&th=1
4 | Gloves | 1 Nos. |  | https://www.uline.com/Product/Detail/S- 15357M/Anti-Static-Gloves/ESD-Gloves- Fingertip-Coated-Medium?model=S- 15357M&RootChecked=yes

## Slide 20: Procedure for Moxa Harness Check
S. N. | Activity Name | Time Taken | No. of Man Power Required
1. | Procedure to check Moxa harness | 07 mins | 01
Total Time Taken |  | 07 Mins | 
Manhour Details:

## Slide 21: Procedure for Moxa Harness Check
Prepared by Rishabh – ME Team
Copyright © 2019 GreyOrange
Safety Precaution:
Turn- OFF the Ranger before starting activity.
Use ESD gloves at all times while performing maintenance work.
Activity should be performed away from Moisture & dust area.
Do not remove any other wires from Ranger while doing the activity.

## Slide 22
Prepared by Rishabh – ME Team
Copyright © 2019 GreyOrange
Step to be followed

## Slide 23: Procedure for Moxa Harness Check
Turn OFF the Ranger by pushing ON/OFF button.
Now move the Ranger on the service lift.
Open front side shell assembly.
Front Side Casing
ON/OFF button

## Slide 24: Now open all the fasteners of top plate and remove it from Ranger
Fasteners of Top Plate
Procedure for Moxa Harness Check

## Slide 25: After removing top plate, it will look as shown in below image.
Procedure for Moxa Harness Check

## Slide 26: Now check the LAN cable of MOXA. It should not be physically damage and connected properly with MOXA.
Procedure for Moxa Harness Check
LAN Cable of MOXA

## Slide 27: Now check the LAN cable of IMB board. It should not be physically damage and connected properly with IMB.
Procedure for Moxa Harness Check
LAN Cable of IMB

## Slide 28: Check the Power Harness of Moxa. It should not be physically damage and connected properly with MOXA.
Procedure for Moxa Harness Check
Power Harness of MOXA

## Slide 29: Check the 12V Power harness of IMB board. It should not be physically damage and connected properly with IMB board.
Procedure for Moxa Harness Check
12V Power Harness of IMB

## Slide 30: Power ON the Ranger. Measure the voltage on Moxa. We should get 12V here.
Procedure for Moxa Harness Check
Measure the voltage here

## Slide 31
END
Return back to error slide for further troubleshooting
Next

## Slide 32
Ranger 3.0 Troubleshooter
Login through Lan cable through 10.3.1.1 as mentioned in support link document.
Again restart the Ranger and check if the issue is resolved.
YES
NO
Is Login issue resolved?
SN | Support Link
1 | Procedure to Login through Lan Cable
Preview
Next

## Slide 33
SN | Version | Prepared / Revised | Checked / Approved |  | Ref Details
1 | 1.0 | Rishabh | Asheesh | Tarun | 
Purpose of Document : Explain the step by step procedure to login into the Ranger through LAN cable at customer site.
Procedure to Login via LAN Cable

## Slide 34
S. N. | Activity Name | Time Taken | No. of Man Power Required
1. | Procedure to login via LAN cable | 05 mins | 01
Total Time Taken |  | 05 Mins | 
Manhour Details:
Procedure to Login via LAN Cable

## Slide 35
Step to be followed:
Turn ON the Ranger. Connect the LAN cable between Ranger LAN port and laptop LAN port.
Procedure to Login via LAN Cable
LAN Port

## Slide 36
Procedure to Login via LAN Cable
Now click on Change adaptor options.

## Slide 37
Procedure to Login via LAN Cable
Now a window will open which is shown in below figure. Here click on connected ethernet option.

## Slide 38
Procedure to Login via LAN Cable
Open network and Internet settings in laptop. After opening of network and internet settings, a window will open which is shown in below figure.

## Slide 39
Procedure to Login via LAN Cable
Now again window will open which is shown in below figure. Here click on Properties option.

## Slide 40
Procedure to Login via LAN Cable
Now again window will open which is shown in below figure. Here scroll down and click on Internet Protocol Version 4 (TCP/IPv4) option and click on Properties option.

## Slide 41
Procedure to Login via LAN Cable
Now again window will open which is shown in below figure.

## Slide 42
Procedure to Login via LAN Cable
Now click on Use the following IP address option and enter the IP address, Subnet Mask, Default gateway, Preferred DNS server as shown in below image. After that click on OK option.

## Slide 43
Procedure to Login via LAN Cable
Now open the mobaxterm application and click on session option.

## Slide 44
ssh gor@10.3.1.1
Procedure to Login via LAN Cable

## Slide 45
ssh gor@10.3.1.1
Procedure to Login via LAN Cable

## Slide 46
Ninja Diagnostic Process
Now it will ask for login as just type gor & press enter key. After that type Password apj0702 and press the enter kay.
Note: If the above window will open after enter IP, it means we have logged in.

## Slide 47
END
Return back to error slide for further troubleshooting
Next

## Slide 48
Ranger 3.0 Troubleshooter
Connect Monitor to IMB board through HDMI cable and check IMB is booting or not as mentioned in support link document.
Again restart the Ranger and check if the issue is resolved.
YES
NO
Is IMB booting through HDMI cable ?
SN | Support Link
1 | Procedure to Login through HDMI Cable
Preview
Next

## Slide 49: Procedure to Login Through HDMI Cable
SN | Version | Prepared / Revised | Checked / Approved |  | Ref Details
1 | 1.0 | Rishabh | Asheesh | Shrinidhi | 
Purpose of Document: Explain the step by step procedure to login into the Ranger via HDMI cable at customer site.

## Slide 50: Procedure to Login Through HDMI Cable
Tools Required :
SN | Item Details | Qty | Photo | Reference Purchase Link
1. | HDMI Cable | 1 Nos. |  | https://www.amazon.in/Quantum-Ethernet-Connectors-Supports-1000Mbps/dp/B098DCLMVL/ref=sr_1_2_sspa?keywords=Lan+Cable&qid=1654078325&sr=8-2-spons&psc=1&spLa=ZW5jcnlwdGVkUXVhbGlmaWVyPUEyVk1ZRDk2OTQ2VzAmZW5jcnlwdGVkSWQ9QTA4OTY3MzIxMDdXUVdRTERHV0pHJmVuY3J5cHRlZEFkSWQ9QTEwMTY2MDcyQjVGNkNINjNSTVYyJndpZGdldE5hbWU9c3BfYXRmJmFjdGlvbj1jbGlja1JlZGlyZWN0JmRvTm90TG9nQ2xpY2s9dHJ1ZQ==
2. | Display | 1 Nos. |  | https://www.amazon.in/LG-22-inch-Gaming-Monitor/dp/B083Y3TYJC/ref=sr_1_4?pf_rd_i=1375425031&pf_rd_m=A1K21FY43GMZF8&pf_rd_p=c4840d55-64bc-4ab2-9807-462cb23b6a17&pf_rd_r=BKJZVAR4078JH1GJGKV0&pf_rd_s=merchandised-search-7&pf_rd_t=101&qid=1655799776&s=computers&sr=1-4&th=1

## Slide 51: Procedure to Login Through HDMI Cable
Prepared by Rishabh – ME Team
Copyright © 2019 GreyOrange
Safety Precaution:
Turn- OFF the Ranger before starting activity.
Use ESD gloves at all times while performing maintenance work.
Activity should be performed away from Moisture & dust area.
Do not remove any other wires from Ranger while doing the activity.

## Slide 52
Prepared by Rishabh – ME Team
Copyright © 2019 GreyOrange
Step to be followed

## Slide 53: Procedure to Login Through HDMI Cable
Turn OFF the Ranger by pushing ON/OFF button.
Now move the Ranger on service trolly with help of the service lift.
Open front side shell assembly.
Front Side Casing
ON/OFF button

## Slide 54: Connect HDMI cable between IMB board and laptop.
Procedure to Login Through HDMI Cable

## Slide 55: Turn- ON the ranger now IMB board should be boot and screen should show as shown in below image.
Procedure to Login Through HDMI Cable

## Slide 56
END
Return back to error slide for further troubleshooting
Next

## Slide 57
Ranger 3.0 Troubleshooter
Check Chassis GND between 12V GND & 48V GND as mentioned in support link document.
Turn-ON the Ranger and check if issue is resolved.
YES
NO
Is login issue resolved ?
SN | Support Link
1 | Procedure to Check 12V & 48V Grounding
Preview
Next

## Slide 58
SN | Version | Prepared / Revised | Checked / Approved |  | Ref Details
1 | 1.0 | Rishabh | Asheesh | Tarun | 
Purpose of Document : Explain the step by step procedure to check grounding between 12V & 48V at customer site.
Procedure to Check Grounding Voltage

## Slide 59
Tools Required :
SN | Item Details | Qty | Photo | Reference Purchase Link
1 | Bit Driver | 1 Nos. |  | https://www.lowes.com/pd/LENOX-6-Piece- Plastic-Handle-Magnetic-Multi-Bit- Screwdriver-Set/1000498761
2 | Bit adaptor | 1 Nos. |  | https://www.amazon.com/uxcell-4-Inch- Drive-Socket- Steel/dp/B07BHFWKDK/ref=sr_1_11?dchild =1&keywords=1%2F4- Inch+Drive+8mm+Hex+Bit+Socket&qid=159 4815613&sr=8-11
3 | Hex Metric M3, bit | 1 Nos. |  | https://www.amazon.com/Wiha-71397- Metric-Insert-6- Piece/dp/B0084B7S70/ref=sr_1_4?dchild=1 &keywords=hex%2Bbits%2Bmetric&qid=15 94814886&sr=8-4&th=1
4 | Gloves | 1 Nos. |  | https://www.uline.com/Product/Detail/S- 15357M/Anti-Static-Gloves/ESD-Gloves- Fingertip-Coated-Medium?model=S- 15357M&RootChecked=yes
5 | Multimeter | 1 Nos. |  | https://robu.in/product/fluke-115-true-rms-field-technicians-digital-multimeter/?gclid=Cj0KCQjwnNyUBhCZARIsAI9AYlGXYD1YFrwn46ex3AJDgSl-jo74ppQLH_HPHHl7tjECMvEsCkGydfoaApb6EALw_wcB
Procedure to Check Grounding Voltage

## Slide 60
Prepared by Rishabh – ME Team
Copyright © 2019 GreyOrange
Safety Precaution:
Turn- OFF the Ranger before starting activity.
Use ESD gloves at all times while preforming maintenance work.
Activity should be performed away from Moisture & dust area.
Do not remove any other wires from Ranger while doing the activity.
Procedure to Check Grounding Voltage

## Slide 61
S. N. | Activity Name | Time Taken | No. of Man Power Required
1. | Procedure to check grounding voltage | 12 mins | 01
Total Time Taken |  | 12 Mins | 
Manhour Details:
Procedure to Check Grounding Voltage

## Slide 62
Step to be followed

## Slide 63
Set the multimeter on voltage and place one probe of multimeter on MOXA GND pin and place second probe of multimeter into any point of chassis GND pin. Voltage should be less than 1 Volt.
Procedure to Check Grounding Voltage
Chassis GND Point
MOXA GND Point
Turn- ON the Ranger by pressing ON/OFF switch.

## Slide 64
Set the multimeter on voltage and place one probe of multimeter on IMB 48V connector GND pin (Black Wire) and place second probe of multimeter on any chassis GND pin. Voltage should be less than 1 Volt.
Procedure to Check Grounding Voltage
Chassis GND Point
IMB 48V connector

## Slide 65
END
Return back to error slide for further troubleshooting
Next

## Slide 66
Ranger 3.0 Troubleshooter
Replace the IMB board as mentioned in support link document.
Again Power ON the Ranger and check if the issue is resolved.
YES
NO
Is login issue resolved?
SN | Support Link
1 | Procedure to Replace the IMB Board
Preview
Next

## Slide 67: Procedure for IMB Assy Replacement
SN | Version | Prepared / Revised | Checked / Approved |  | Ref Details
1 | 1.0 | Rishabh | Shrinidhi | Anand | 
Purpose of Document: Explain the step by step procedure to replace the IMB Assy and testing process at customer site.

## Slide 68: Procedure for IMB Assy Replacement
Tools Required :
SN | Item Details | Qty | Photo | Reference Purchase Link
1 | Bit Driver | 1 Nos. |  | https://www.lowes.com/pd/LENOX-6-Piece- Plastic-Handle-Magnetic-Multi-Bit- Screwdriver-Set/1000498761
2 | Bit adaptor | 1 Nos. |  | https://www.amazon.com/uxcell-4-Inch- Drive-Socket- Steel/dp/B07BHFWKDK/ref=sr_1_11?dchild =1&keywords=1%2F4- Inch+Drive+8mm+Hex+Bit+Socket&qid=159 4815613&sr=8-11
3 | Hex Metric M3, bit | 1 Nos. |  | https://www.amazon.com/Wiha-71397- Metric-Insert-6- Piece/dp/B0084B7S70/ref=sr_1_4?dchild=1 &keywords=hex%2Bbits%2Bmetric&qid=15 94814886&sr=8-4&th=1
4 | Gloves | 1 Nos. |  | https://www.uline.com/Product/Detail/S- 15357M/Anti-Static-Gloves/ESD-Gloves- Fingertip-Coated-Medium?model=S- 15357M&RootChecked=yes

## Slide 69: Procedure for IMB Assy Replacement
S. N. | Activity Name | Time Taken | No. of Man Power Required
1. | Shell/Casing Assembly & Dis-assembly | 10 mins | 01
2. | IMB Replacement | 07 mins | 
3. | Diagnostic test | 12 mins | 
Total Time Taken |  | 29 Mins | 
Manhour Details:

## Slide 70: Step to be Followed

## Slide 71: Procedure for IMB Assy Replacement
Turn OFF the Ranger by pushing the ON/OFF button.
Move the Ranger on service trolly with the help of service lift.
Open Front side Casing assembly.
Front side casing assembly
ON/OFF button

## Slide 72: Procedure for IMB Assy Replacement Now open the fasteners of top plate and remove it from Ranger.
Fasteners

## Slide 73: Procedure for IMB Assy Replacement After removing top plate, it will look as shown in below image.

## Slide 74: Procedure for IMB Assy Replacement Now disconnect the main Rear Connector from IMB Assy.
Main Rear Connector

## Slide 75: Procedure for IMB Assy Replacement Now disconnect the main Front Connector from IMB Assy.
Main Front Connector

## Slide 76: Procedure for IMB Assy Replacement Now remove the bottom camera harness from doggle.
Bottom Camera Harness

## Slide 77: Procedure for IMB Assy Replacement Now disconnect IMB 48V Power connector from IMB Assy.
IMB 48V Power Connector

## Slide 78: Procedure for IMB Assy Replacement Now disconnect 12V Power connector from IMB Assy.
12V Power Connector

## Slide 79: Procedure for IMB Assy Replacement Now disconnect the Top cam connector and LAN cable from IMB Assy.
Top Camera Connector
LAN Cable

## Slide 80: Procedure for IMB Assy Replacement Now open all the fasteners of IMB assembly and remove it from Ranger.
IMB Assembly Fasteners

## Slide 81: Procedure for IMB Assy Replacement After removing IMB assembly from Ranger, it will look as shown in below image. Now mount new IMB assembly and tight all the fasteners giving torque value 15-18NM.

## Slide 82: Connect back all the respective harness in reverse form.

## Slide 83: Procedure for IMB Assy Replacement Now mount the top plate on the bot 3,0 and tight all the bolts giving torque 42-46 NM.

## Slide 84: Procedure for IMB Assy Replacement
Now mount both shell/casing assembly on butler and mount all the respective fasteners giving torque 4.5-8.5 NM .
Shell Assy

## Slide 85: Procedure for IMB Assy Replacement
Perform Diagnostic and check if the issue is resolved.

## Slide 86
END
Return back to error slide for further troubleshooting
Next

## Slide 87
Ranger 3.0 Troubleshooter
Replace the Moxa board as mentioned in support link document.
Again Power ON the Ranger and check if the issue is resolved.
YES
NO
Is login issue resolved?
SN | Support Link
1 | Procedure to Replace the MOXA Board
Preview
Next

## Slide 88
SN | Version | Prepared / Revised | Checked / Approved |  | Ref Details
1 | 1.0 | Rishabh | Asheesh | Shrinidhi | 
Purpose of Document: Explain the step by step procedure to replace MOXA at customer site.
Procedure to Replace MOXA

## Slide 89
Tools Required :
SN | Item Details | Qty | Photo | Reference Purchase Link
1 | Bit Driver | 1 Nos. |  | https://www.lowes.com/pd/LENOX-6-Piece- Plastic-Handle-Magnetic-Multi-Bit- Screwdriver-Set/1000498761
2 | Bit adaptor | 1 Nos. |  | https://www.amazon.com/uxcell-4-Inch- Drive-Socket- Steel/dp/B07BHFWKDK/ref=sr_1_11?dchild =1&keywords=1%2F4- Inch+Drive+8mm+Hex+Bit+Socket&qid=159 4815613&sr=8-11
3 | Hex Metric M3, bit | 1 Nos. |  | https://www.amazon.com/Wiha-71397- Metric-Insert-6- Piece/dp/B0084B7S70/ref=sr_1_4?dchild=1 &keywords=hex%2Bbits%2Bmetric&qid=15 94814886&sr=8-4&th=1
4 | Gloves | 1 Nos. |  | https://www.uline.com/Product/Detail/S- 15357M/Anti-Static-Gloves/ESD-Gloves- Fingertip-Coated-Medium?model=S- 15357M&RootChecked=yes
5 | Ninja Portable Charger | 1 Nos. | - | 
Procedure to Replace MOXA

## Slide 90
Prepared by Rishabh – ME Team
Copyright © 2019 GreyOrange
Safety Precaution:
Turn- OFF the Ranger before starting activity.
Use ESD gloves at all times while performing maintenance work.
Activity should be performed away from Moisture & dust area.
Do not remove any other wires from Ranger while doing the activity.
Procedure to Replace MOXA

## Slide 91
S. N. | Activity Name | Time Taken | No. of Man Power Required
1. | Shell/Casing Assembly & Dis-assembly | 10 mins | 01
2. | Moxa Replacement | 05 mins | 
3. | Login Bot | 02 mins | 
Total Time Taken |  | 17 Mins | 
Manhour Details:
Procedure to Replace MOXA

## Slide 92
Prepared by Rishabh – ME Team
Copyright © 2019 GreyOrange
Step to be followed

## Slide 93
Turn OFF the Ranger by pushing ON/OFF button.
Now move the Ranger on the service lift.
Open front side shell assembly.
Front Side Casing
ON/OFF button
Procedure to Replace MOXA

## Slide 94: Remove Power harness of MOXA with the help of screw driver.
Procedure to Replace MOXA
Power Harness

## Slide 95: Remove both LAN cable from MOXA.
Procedure to Replace MOXA
LAN Cable

## Slide 96: Now remove MOXA and replace it from Ranger. Now mount new moxa on Ranger. Login into Ranger through IP and check if the issue is resolved.
Procedure to Replace MOXA
MOXA

## Slide 97
END
Return back to error slide for further troubleshooting
Next

## Slide 98
Ranger 3.0 Troubleshooter
Check battery voltage of Ranger as mentioned in support link document.
YES
NO
Is Battery Voltage correct?
SN | Support Link
1 | Procedure to Check Battery Voltage
Preview
Next

## Slide 99
SN | Version | Prepared / Revised | Checked / Approved |  | Ref Details
1 | 1.0 | Rishabh | Asheesh | Shrinidhi | 
Purpose of Document: Explain the step by step procedure to check the battery voltage at customer site.
Procedure to Check Battery Voltage

## Slide 100
Tools Required :
SN | Item Details | Qty | Photo | Reference Purchase Link
1 | Multimeter | 1 Nos. |  | https://www.industrybuying.com/digital-multimeters-fluke-ME.EL.DI.191486/?utm_source=Google&utm_medium=PLA&utm_campaign=PLAPMAX_BR_Plan_Inventory&gclid=Cj0KCQjwnNyUBhCZARIsAI9AYlGx3580YddYFFGOQ5ATytrZhpDUQX1Y8X4Csr8WSBQwUzsQKe-Z6xwaAjI8EALw_wcB
2 | Gloves | 1 Nos. |  | https://www.uline.com/Product/Detail/S- 15357M/Anti-Static-Gloves/ESD-Gloves- Fingertip-Coated-Medium?model=S- 15357M&RootChecked=yes
Procedure to Check Battery Voltage

## Slide 101
Prepared by Rishabh – ME Team
Copyright © 2019 GreyOrange
Safety Precaution:
Turn- OFF the Ranger before starting activity.
Use ESD gloves at all times while performing maintenance work.
Activity should be performed away from Moisture & dust area.
Do not remove any other wires from Ranger while doing the activity.
Procedure to Check Battery Voltage

## Slide 102
S. N. | Activity Name | Time Taken | No. of Man Power Required
1. | Measure Battery Voltage | 01 mins | 01
Total Time Taken |  | 01 Mins | 
Manhour Details:
Procedure to Check Battery Voltage

## Slide 103
Prepared by Rishabh – ME Team
Copyright © 2019 GreyOrange
Step to be followed

## Slide 104
Turn OFF the Ranger by pushing ON/OFF button.
ON/OFF button
Procedure to Check Battery Voltage

## Slide 105
Note: 1.) Battery voltage should be greater than 51V.
2.) Don’t short the multimeter probe. It may damage the battery.
Measure the battery voltage on staubli connector of Ranger. It should not be less than 50V. If we found the battery voltage less than 50V, we should charge the battery.
Procedure to Check Battery Voltage
Staubli Connector Pins where we
should measure voltage.

## Slide 106
END
Return back to error slide for further troubleshooting
Next

## Slide 107
Ranger 3.0 Troubleshooter
Replace the battery assembly as mentioned in support link document.
Again power ON the Ranger and check if the issue is resolved.
YES
NO
Is Power issue resolved?
SN | Support Link
1 | Procedure to Replacement of Battery Assembly
Preview
Next

## Slide 108
Procedure For Battery Pack Replacement
SN | Version | Prepared / Revised | Checked / Approved |  | Ref Details
1 | 1.0 | Rishabh | Asheesh | Shrinidhi | 
Purpose of Document : Explain the step by step procedure for battery pack replacement at customer sites.

## Slide 109
Tools Required :
SN | Item Details | Qty | Photo | Reference Purchase Link
1 | Bit Driver | 1 Nos. |  | https://www.lowes.com/pd/LENOX-6-Piece- Plastic-Handle-Magnetic-Multi-Bit- Screwdriver-Set/1000498761
2 | Bit adaptor | 1 Nos. |  | https://www.amazon.com/uxcell-4-Inch- Drive-Socket- Steel/dp/B07BHFWKDK/ref=sr_1_11?dchild =1&keywords=1%2F4- Inch+Drive+8mm+Hex+Bit+Socket&qid=159 4815613&sr=8-11
3 | Hex Metric M3, M4 bit | 1 Nos. |  | https://www.amazon.com/Wiha-71397- Metric-Insert-6- Piece/dp/B0084B7S70/ref=sr_1_4?dchild=1 &keywords=hex%2Bbits%2Bmetric&qid=15 94814886&sr=8-4&th=1
4 | Gloves | 1 Nos. |  | https://www.uline.com/Product/Detail/S- 15357M/Anti-Static-Gloves/ESD-Gloves- Fingertip-Coated-Medium?model=S- 15357M&RootChecked=yes
Procedure For Battery Pack Replacement

## Slide 110
S. N. | Activity Name | Time Taken | No. of Man Power Required
1. | Shell/Casing Assembly & Dis-assembly | 10 mins | 01
2. | Battery Pack Replacement | 07 mins | 
3. | BMS Diagnostic | 05 mins | 
Total Time Taken |  | 22 Mins | 
Manhour Details:
Procedure For Battery Pack Replacement

## Slide 111
Safety Precaution:
Turn- OFF the Ranger before starting activity.
Use ESD gloves at all times while preforming maintenance work.
Activity should be performed away from Moisture & dust area.
Do not remove any other wires from Ranger while doing the activity.
Procedure For Battery Pack Replacement

## Slide 112
Step to be Followed

## Slide 113
Turn OFF the Ranger by pushing ON/OFF button.
Now move the Ranger on service trolly with help of the service lift.
Open front side shell assembly.
Front Side Casing
ON/OFF button
Procedure For Battery Pack Replacement

## Slide 114
Procedure For Battery Pack Replacement

## Slide 115
Remove the Discharge connector & Charge connector from battery pack.
Discharge Connector
Procedure For Battery Pack Replacement
Charge Connector

## Slide 116
Circular Connector
Procedure For Battery Pack Replacement
Remove both circular connector from battery pack.

## Slide 117
Open the fastener of battery pack and remove it from Ranger. Again mount the new battery pack and tight its fasteners giving torque 20-30 NM.
Procedure For Battery Pack Replacement
Fastener

## Slide 118
END
Return back to error slide for further troubleshooting
Next

## Slide 119
Ranger 3.0 Troubleshooter
Charge the battery as mentioned in support link document.
Again power ON the Ranger through ON/OFF switch and check if issue is resolved.
YES
NO
Is Power ON issue resolved?
SN | Support Link
1 | Procedure to Charge the Battery
Preview
Next

## Slide 120
SN | Version | Prepared / Revised | Checked / Approved |  | Ref Details
1 | 1.0 | Rishabh | Asheesh | Shrinidhi | 
Purpose of Document: Explain the step by step procedure to charge the battery at customer site.
Procedure to Charge Battery

## Slide 121
Tools Required :
SN | Item Details | Qty | Photo | Reference Purchase Link
1 | Bit Driver | 1 Nos. |  | https://www.lowes.com/pd/LENOX-6-Piece- Plastic-Handle-Magnetic-Multi-Bit- Screwdriver-Set/1000498761
2 | Bit adaptor | 1 Nos. |  | https://www.amazon.com/uxcell-4-Inch- Drive-Socket- Steel/dp/B07BHFWKDK/ref=sr_1_11?dchild =1&keywords=1%2F4- Inch+Drive+8mm+Hex+Bit+Socket&qid=159 4815613&sr=8-11
3 | Hex Metric M3, bit | 1 Nos. |  | https://www.amazon.com/Wiha-71397- Metric-Insert-6- Piece/dp/B0084B7S70/ref=sr_1_4?dchild=1 &keywords=hex%2Bbits%2Bmetric&qid=15 94814886&sr=8-4&th=1
4 | Gloves | 1 Nos. |  | https://www.uline.com/Product/Detail/S- 15357M/Anti-Static-Gloves/ESD-Gloves- Fingertip-Coated-Medium?model=S- 15357M&RootChecked=yes
5 | Ninja Portable Charger | 1 Nos. | - | 
Procedure to Charge Battery

## Slide 122
S. N. | Activity Name | Time Taken | No. of Man Power Required
1. | Procedure to charger battery | 60 mins | 01
Total Time Taken |  | 60 Mins | 
Manhour Details:
Procedure to Charge Battery

## Slide 123
Prepared by Rishabh – ME Team
Copyright © 2019 GreyOrange
Safety Precaution:
Turn- OFF the Ranger before starting activity.
Use ESD gloves at all times while preforming maintenance work.
Activity should be performed away from Moisture & dust area.
Do not remove any other wires from Ranger while doing the activity.
Procedure to Charge Battery

## Slide 124
Prepared by Rishabh – ME Team
Copyright © 2019 GreyOrange
Step to be followed

## Slide 125
Turn OFF the Ranger by pushing ON/OFF button.
Now move the Ranger on the service lift.
Open front side shell assembly.
Front Side Casing
ON/OFF button
Procedure to Charge Battery

## Slide 126: Connect charging connector on charging port of battery. Turn- ON the charger power and charge the battery.
Note: Please use Ninja specific portable charger for charging so that we can prevent the battery from overcharge or damage.
Procedure to Charge Battery
Charge Connector

## Slide 127
END
Return back to error slide for further troubleshooting
Next

## Slide 128
Ranger 3.0 Troubleshooter
Again restart the Ranger and check if the issue is resolved.
Preview
Next
YES
NO
Is Power ON issue resolved?

## Slide 129
Ranger 3.0 Troubleshooter
Done
If previous steps could not resolve the issue, create a site support ticket for resolution of error.
Preview
Next

## Slide 130
Ranger 3.0 Troubleshooter
Begin Again
END OF TROUBLESHOOT